## Slide 1: ROM SAF PTM18 IEEC, Barcelona 31-05-2016
DMI ROPP developments:
Recent and coming updates to dmi_trunk
Stig Syndergaard

## Slide 2: Purpose of the dmi_trunk
A well-maintained branch of ROPP
Used at DMI as our main ROPP development branch (thus, it is our ‘trunk’)
Usually the latest ROPP release + development made at DMI
dmi_trunk is upgraded whenever a new ROPP is released: merge of new ROPP and current dmi_trunk
dmi_trunk is the ROPP software that we use in operations (when we make a GPAC upgrade)
Development work at DMI always take the starting point in dmi_trunk (typically making a branch from dmi_trunk and merge back when done)
Currently at dmi_trunk_8.1 (ROPP 8.1 + DMI developments)
Over time, we strive to keep dmi_trunk ≅ ROPP (facilitating next merges of ROPP and dmi_trunk)
  Developments in dmi_trunk should become part of a next ROPP release (possibly internal release; upon agreement with Met Office)
  Philosophy: if it is needed for us, then it is also useful for others
  Where things can be done in different ways, we always adhere to the way things are done in ROPP (to facilitate future merges)
  We regularly forward our changes to Met Office in advance of a ROPP GG meeting or new ROPP release

## Slide 3: Recent updates to dmi_trunk
Final adjustments for including ropp_pp_invert_tool.f90 into ropp_pp_occ_tool.f90
    ropp_pp_invert_tool is now obsolete; ropp_pp_occ_tool processes from lev1b with -inv option
Changes to ropp_pp_occ_tool.f90 and related subroutines
  Optionally calculate tangent points (lat_tp, lon_tp) to account for bending (thanks to Chris Burrows)
Changes to occ_point.f90 and tangent_point.f90
  Fixed problem with occultation point determination on an ellipsoid – error for north-south going GNSS-LEO lines was of the size of the difference between geographic and geocentric latitude (Simon later found a more mathematically correct solution, but it is not yet implemented)
Minor change to ropp_pp_preprocess_cosmic.f90
  Now returning fatal error (instead of just info) when navigation bit file is not found
Change to ropp_fm_abel.f90
  Now returns bending angles on all observational heights, also above the state vector top
Change to ropp_pp_ionospheric_correction.f90
  Now always using w_smooth as in ‘implementation from OCC’ (fixing smoothing bug #2)
Minor changes to README.ropp, build_ropp, roppauto, roppconfig
  Included ropp_apps in installation scripts

## Slide 4: Recent updates to dmi_trunk (cont.)
Change to ropp_pp_types.f90
  Longer strings for mfile, bfile, navfile (to be consistent with previous change in ropp_pp tools)
Changes to ropp_io_read_ncdf_get.f90
  Determine open loop bit based on ol_data_used flag, not on ol_data_available/rs_data_available
  Settings of PCD bits in ropp_io_read_ucardata_atmPhs and ropp_io_read_ucardata_atmPrf routines
Change to ropp_io_assign.f90
  Copying the %bg substructure of Roprof
Changes to ropp_fm_bg2ro_1d.f90
  Implemented forward-modeling to dry_temp. This required adding two new routines in ropp_fm/refrac_1d, changing the interfaces in ropp_fm.f90, and minor changes to two Makefile.am files.
  Now copying only height variables when initializing with the -l option, not the whole lev1b and lev2a structures
  New routines to initialize the Obs1dRefrac and Obs1dBangle structures when called with the -l option
Minor changes to grib2bgrasc.f90
  Now setting PCD bit 15 (background data)
  Now using fcperiod (lead time) from grib1 when interpolating in time (still debating on that one)

## Slide 5: Recent updates to dmi_trunk (cont.)
Change to ropp_apps_tph_tool.f90
  Avoiding extra variables stored in Vlist to be lost
Minor change to ropp_io_types.f90
  Changed Level 2b shum valid range from 5 g/kg to 50 g/kg (still debating on that one, see #437)
Minor changes to eum2ropp, ucar2ropp, ropp2ropp, and ropp_fm_bg2ro_1d
  No warnings (exit code 1) when using --no-ranchk or --no-zapem options

## Slide 6: Coming updates to dmi_trunk
Fixes to ropp_pp_occ_tool (problems originally detected with ropp_pp_invert_tool)
  Related to poor input data – the code needs to be able to handle them better (must not hang or give segmentation faults) (tickets #319, #332, #358, #374, #442)
  Possibly more fixes after looking into odd case from JGR paper by Wang et al. (ticket #344)
More global attributes (harmonizing with our level 3 products)
  Introducing description, product_id, product_name, product_acronym, product_version, etc. (ticket #342)
Possibly more changes to eum2ropp
  Level 1a parts in connection with our reprocessing (ticket #370)
Possibly changes to ropp_fm_bg2ro
  Problems with using the -l option (output on observation levels) when input level 1b levels are severely out of order (ticket #334)
Changes to ropp_pp_occ_tool
    To make sure that profiles now failing to process because of e.g., stat.opt. problems are still processed, but with relevant QC parameters written to the NetCDF output file (tickets #317, #441)
Possibly more changes to ropp_pp_occ_tool subroutines
  Subroutines related to the wave optics part to deal with kink at 25 km (no ticket yet)